## Slide 1: Optimization of a Heat Exchanger with Turbulent Flow

## Slide 2: Optimization Setup
Control and heat
The translation and scaling of the pipes is handled by the Transformation feature
Both fluids are water with inlet temperatures of 30 oC and 80 oC
Fluid
The flow is pressure driven and the objective is to maximize the heat transfer
The Reynolds number is approximately 10,000. The k-epsilon turbulence model is used
Optimization of a Heat Exchanger with Turbulent Flow

## Slide 3: Result
Discussion
Some pipes should be larger. Some should be smaller. All are moved a bit. There is a tendency for bigger pipes towards smaller pipes near the center.
Performance
The heat transfer rate is improved by around 20 %.
Manufacturing
The design is qualitatively identical to the starting point so manufacturing ought to be possible
Perspective
Practical heat exchanger often use more pipes and more segments, which might explains why the efficiency is only around 50 %
Non-uniform pipe size can improve performance