## Slide 1: Stray Currents from a Train in a Light Railway Transit System

## Slide 2: Introduction
Light railway transit (LRT) systems often utilize DC power for train propulsion
In these systems the potential gradients in the rails may induce stray currents, which corrode nearby metallic structures
In this example the Cathodic Protection interface, using Edge Electrode nodes, is used to model stray currents at a pipe for different train locations
The 3D domain surrounding the railway and the pipe features different soil conductivities
The impact of changed soil conductivities and pipe position is also investigated
This Photo by Unknown Author is licensed under CC BY-SA

## Slide 3: Geometry
Two parallel rails are located between two traction substations (TSS) over a 3D soil profile
  Rails sit on ties and gravel
  1.2 km between the stations
Stray currents originate from the current returning through the rails from the train to the traction substations
Soil profile confined by insulating rock
  Area 1.77 km2
  Maximum clay depth 20 m
Sandy clay
Tracks
Pipe
Pond
Clay
TSS 1
TSS 2
Gravel
Ties
Rails

## Slide 4: Rails and Pipe
Cathodic Protection, Edge Electrode nodes
  The Electrode Reaction features define stray current leaving and entering rails and pipe due to electrochemical reactions
  Reaction expression taken from Q235 steel in soil available in Material Library, Corrosion
  Electrode Current features at TSS 1 define total currents per rail , ITSS1. Function of train location, xtrain, and current, Itrain, for the rail length, Lrail:
  Electric Potential feature sets potential equal to 0 at TSS 2, grounded
Current source in rails at train location
  Added with the Weak Contribution feature

## Slide 5: Conductivities
Electrolyte conductivities defined individually for each material in the soil using user-defined values
Anisotropic electrolyte conductivity set at ties

## Slide 6: Train Propulsion Functions
Train propulsion current depends on acceleration, braking, and idle periods
Traction substations supply the current
Current
Traveled distance over time to define train location
Location
Positioning of train on rails with Gaussian pulse representation (integrated value equal 1)
Gaussian-pulse shaped current drawn at train location
Shape

## Slide 7: Study
Parametric sweep to investigate three different scenarios:
  Base scenario, sand= 400 m and LRePos=0 m
  Sandy clay treated as clay, sand = clay= 50 m
  Pipe repositioned +50 m in y-direction, LRePos=50 m
To vary the train location, a Stationary Study step using Auxiliary sweep for the traveled time, t_train, is used

## Slide 8: Currents and Train Location
Simulated TSS currents

## Slide 9: Base Scenario Results
Soil potential and current

## Slide 10: Base Scenario Results
Rail potential

## Slide 11: Base Scenario Results
Stray current density rails

## Slide 12: Base Scenario Results
Current density at pipe

## Slide 13: Comparison Results
Higher resistivity in soil reduces the corrosion rate
Repositioning of pipe has an impact on the rate
Pipe corrosion rate for the investigated scenarios at 52 s

## Slide 14: References
Z. Cai, X. Zhang, and H. Cheng, “Evaluation of DC-Subway Stray Current Corrosion With Integrated Multi-Physical Modeling and Electrochemical Analysis,” IEEE Access, vol. 7, 168404, 2019. http://doi.org/10.1109/ACCESS.2019.2953960
S. Aatif, H. Hu, F. Rafiq, and Z. He, “Analysis of rail potential and stray current in MVDC railway electrification system,” Railway Engineering Science, vol. 29, 394, 2019. http://doi.org/10.1007/s40534-021-00243-0
G. Du, D. Zhang, G. Li, C. Wang, and J. Liu, “Evaluation of Rail Potential Based on Power Distribution in DC Traction Power Systems,” Energies, vol. 9, 729, 2016. http://doi.org/10.3390/en9090729