## Slide 1: Simulation of the Spatial Response of Speakers and Microphones … and feedback/echo problems
COMSOL

## Slide 2: Content
Use of simulation
Feedback/echo
  Acoustic domain
  Vibroacoustic domain
Modeling strategies
  Full multiphysics
  Lumped multiphysics
Conference Speaker System Example
HRTF and manikins
“Full” virtual test setup
Laptop speaker spatial response at 20 kHz
Notes: Ed: I suggest changed indentation. It “steals” too much space in the current template, see my suggested change in the slide master.
Ed: I suggest Courier for code snippets. Cambria Math and Symbol for equations: 𝑎^2+𝑏^2=𝑐^2; 𝐴=𝜋𝑟^2

## Slide 3: Content
Use of simulation
Feedback/echo
  Acoustic domain
  Vibroacoustic domain
Modeling strategies
  Full multiphysics
  Lumped multiphysics
Conference Speaker System Example
HRTF and manikins
“Full” virtual test setup
Conference speaker system at 2 kHz

## Slide 4: Content
Use of simulation
Feedback/echo
  Acoustic domain
  Vibroacoustic domain
Modeling strategies
  Full multiphysics
  Lumped multiphysics
Conference Speaker System Example
HRTF and manikins
“Full” virtual test setup
“Full” virtual test setup at 1 kHz

## Slide 5: Use of Simulation …
Why?
Virtual development and prototypes
Concept and design phase
  Involve industrial designers
Front loading
Decision making
Problem solving/identification
What?
Optimized performance
Input to DSP and algorithm developers
  Transfer functions
  Microphone directivity (multi-mic system) etc.
Identify mechanical/model problems
General acoustic performance

## Slide 6: Feedback and Echo
DSP
electronics
acoustic
feedback path
vibration or
vibroacoustic
communication
system
speaker
mic.

## Slide 7: Feedback and Echo
acoustic
feedback path
vibration or
vibroacoustic
communication
system
in
out
speaker
mic.

## Slide 8: Modeling Strategies
Full multiphysics model
  Electromagnetic
  Structural
  Acoustic
  Thermoviscous acoustics
Lumped multiphysics approaches
  Thiele-Small representation
  Impedance
  Transfer matrix representation
  Impedance models for perforates etc.
GUI example from COMSOL. Lumped port with an electroacoustic two-port representation.
www.comsol.com/acoustics-module

## Slide 9: Speaker: Full Multiphysics FEM
  Ole Wolff OWS-1943T-8CP microspeaker (discontinued model). Copyright by Ole Wolff Elektronik A/S.

## Slide 10: Speaker: Full Multiphysics FEM
3D microspeaker
2D axisymmetric

## Slide 11: Speaker: Hybrid TS-FEM
uD
  Thiele-Small representation of the electromechanical part of the speaker. System solved as an electric circuit and can have any desired complexity.

## Slide 12: Microphone
Microphone modeled as an impedance
Microphone/waveguide modeled as a lumped electroacoustic system
  Lumped port
  Transfer matrix representation
Modeling of thermoviscous losses in mesh/perforates and small ducts
All are built-in options ready to use in COMSOL Multiphysics
GUI example from COMSOL. Lumped port with an electroacoustic two-port representation.

## Slide 13: Microphone
exterior
acoustic
waveguide
transducer
mesh/grill

## Slide 14: Microphone
exterior
acoustic
waveguide
transducer
mesh/grill
impedance Z
Impedance Z
Measured data
Detailed simulation

## Slide 15: Microphone
exterior
acoustic
waveguide
transducer
mesh/grill
T
Transfer matric T
Measured data
Detailed simulation

## Slide 16: Microphone
exterior
acoustic
waveguide
transducer
mesh/grill
T
Transfer matric T
Measured data
Detailed simulation

## Slide 17: Feedback and Echo: Example
Lump speaker
microphone
interior air
air (FEM)
air (BEM)
perforated plate
microphone

## Slide 18: Spatial Response: Speaker
Exterior pressure field from the conference speaker. Here visualized at 6300 Hz

## Slide 19: Spatial Response: Speaker

## Slide 20: Spatial Response: Directional Microphone
1 = 0[deg]
2 = 90[deg]
3 = 180[deg]
Reciprocity
  Use the microphone as source
  Assign complex phase to each: exp(i )

## Slide 21: HRTF and Manikins
Communication perspective:
  Wearables, open shoulder mounted units, smart gear etc.
Examples:
  https://www.comsol.com/model/head-and-torso-simulator-acoustics-74381
  https://www.comsol.com/model/head-and-torso-hrtf-computation-75011

## Slide 22: Full Virtual Test Setup
Speaker in conference speaker system as source.
Acoustic manikin mouth as source.

## Slide 23: Conclusions
Consider what electroacoustic/acoustic representation is needed!
Start simple!
You do not always need to go full multiphysics
Use the knowledge you have from lumped models and measurements
Measure the transfer-matrix of sub systems
Build-up the complexity
www.comsol.com/acoustics-module