## Slide 1: MEMS Scanning Mirror
COMSOL

## Slide 2: Model Definition
Single-axis electrostatically driven scanning micromirror:
  A reflector attached to two anchor points by two torsion beams
  A vertical comb drive structure formed by moving combs on the mirror sides and fixed combs on the device layer
Model the mirror torsional motion caused by a driving voltage:
  Range: 0~300 V
Validation of an analytical expression for the electromechanic force
Moving combs
Fixed combs
Reflector
Torsion beam
Device layer
Isolator layer
Base layer
Anchor point

## Slide 3: Comparison of Methods for Electromechanics
Analytical Expression
Advantages: low computational effort and large angle rotations without moving mesh
Disadvantages: limited to cases with fixed motion trajectories
Electromechanics Interface
Advantages: predefined multiphysics coupling that can handle any deformation
Disadvantages: longer computation time and requires moving mesh

## Slide 4: Analytical Expression
Electrostatic moments on rotating combs
The capacitance function, C, is unknown:
  A set of capacitance values can be computed by varying the rotation angle
  A function can be fitted to the computed capacitance data, for example a Gaussian process function

## Slide 5: Implementation in COMSOL Multiphysics®
Electrostatic
Calculation of the capacitance between the driven and fixed combs and its sensitivity to the mirror rotation angle
Solid Mechanics
Calculation of the torsion angle of a mirror under the action of an electrostatic driving moment

## Slide 6: MODEL DEFINITION, ELECTROSTATICS INTERFACE: Computation of the Electrostatic Moments
Parametric sweep of the rotation angle of the reflector
Calculation of the comb capacitance as a function of the mirror rotation angle:
Derivation of the comb capacitance with respect to the rotation angle:
Moment of the driving combs:

## Slide 7: MODEL DEFINITION, SOLID MECHANICS INTERFACE: Computation of the Rotation Angle
Electrostatic moments defined as loads using rigid connectors
A parametric sweep is used to vary the driving voltage
The rotation angle is computed using an arcsin function

## Slide 8: ELECTROSTATICS Model Parameters
Rotation angle
  Angle of twist of the mirror around the axis of rotation
Driving voltage

## Slide 9: ELECTROSTATICS Geometry Parameters
Rotation angle: angle of the mirror surface in relation to its undeformed position

## Slide 10: ELECTROSTATICS BC: Terminal 1
Activating terminal: used to calculate capacitance, the exact value of the voltage is not important, i.e., it can be set to V0 = 1V

## Slide 11: ELECTROSTATICS BC: Terminal 2
Floating voltage:
  Terminals 1 and 2 are turned on alternately during operation
  Due to the symmetry, only one side is computed

## Slide 12: ELECTROSTATICS BC: Grounded
Mirror and moving combs are grounded.

## Slide 13: ELECTROSTATICS Study: Surrogate Model Training
The study performs a parametric sweep of the mirror rotation angle, calculates the capacitance for each angle, and creates a surrogate model.

## Slide 14: ELECTROSTATICS Results: Capacitance Function
A Gaussian Process function is fitted to capacitance data:

## Slide 15: ELECTROSTATICS Results: Force-Electric Coupling Coefficient
Derivation of the fitted function yields the force-electric coupling coefficient :

## Slide 16: SOLID MECHANICS Variables
Rotation angle:
  Rotation angle of the mirror under an electrostatic moment
Electrostatic moments:
  Calculated by force-electric coupling coefficients:

## Slide 17: SOLID MECHANICS Fixed Constraints
The scanning mirror is fixed at the bottom of the frame.

## Slide 18: SOLID MECHANICS Rigid Connector
An electrostatic moment is applied on the drive combs.

## Slide 19: SOLID MECHANICS Study: Auxiliary Sweep
The driving voltage is varied in an auxiliary sweep to calculate the rotation angles.

## Slide 20: SOLID MECHANICS Results
Rotation angle at different driving voltages

## Slide 21: Analytic Expression vs. Electromechanics Interface
Results are in good agreement
Computing time for a sweep range of 10-100 V:
  Analytic expression: 2 m 13 s
  Electromechanics interface: 4 h 40 m
The difference between the two methods increases with voltage.

## Slide 22: Dynamic Analysis
Mode analysis:
  Search the eigenfrequencies corresponding to torsional modes
Time-dependent analysis:
  Simulation of startup of the oscillation process

## Slide 23: Optical Scanning Using Ray Optics
Coupling between the Solid Mechanics and Geometrical Optics interfaces
Uniaxial torsion enables 1D scanning
Biaxial torsion for 2D surface scanning