## Slide 1: Modeling the 3-𝜔 Method with Frequency-Domain Analysis of Heat Transfer

## Slide 2: Background
The 3-𝜔 method is an experimental technique to estimate the thermal conductivity k of nanostructured material sample [1].
An AC current at frequency f is applied in a narrow metal strip of length L and width w deposited onto the sample.
It induces a periodic Joule heating with an amplitude as well as temperature oscillations .
Schematic image of the sample and the heater.
Narrow heater strip
Sample
Connector pads
L
w

## Slide 3: Background
log-linear region
The equation relating the thermal conductivity to the temperature oscillations amplitude of the narrow heater strip in a semi-infinite solid can be approximated as [2]:
If the width of the heater strip, w, is much lesser than the thermal penetration depth, becomes constant and the thermal conductivity of the sample can be estimated using the Cahill’s equation:
To ensure the chosen frequencies correspond to the log-linear approximation range, we sweep through wide range of frequencies to find out such a log-linear region for any given conditions.
Average temperature oscillation amplitude vs frequency.

## Slide 4: Model Definition Geometry & Model Assumptions
2D symmetrical cross section of the sample
  Only one half of the section is modeled
  w = 0.1 mm, d = 0.3 mm
Physical properties of the sample are constant
The radiation and convection losses are negligable
Sample is semi-infinite solid
  The “infinite domains” (shown in blue color) are used
The heat flux q at the interface between the metal strip and the sample is uniform
2D model geometry.
d
3w
w/2
q

## Slide 5: Model Definition Boundary Conditions
Boundary Heat Source on the surface of the heater
  Time Dependent Analysis: the heat rate is defined as harmonic function of time
  Frequency Domain Analysis: the amplitude of the heat rate oscillations is defined, Harmonic Perturbation option is activated
Temperature on the lower external boundary
Symmetry on the left external boundary
Thermal Insulation on the remaining external boundaries

## Slide 6: Model Definition Approach 1: Time Dependent Analysis
Solves the transient heat transfer equation with the Time Dependent solver
  Time Dependent study step is used to compute the temporal evolution of average heater temperature. The transient heat transfer is modeled within N periods of heat rate oscillations
  Time to Frequency FFT study step performs the fast Fourier transform to evaluate the amplitude of temperature oscillations
  Parametric Sweep is used to sweep over the frequency range to find the log-linear region

## Slide 7: Model Definition Approach 2: Frequency Domain Analysis
Frequency-Domain Perturbation study type is used to analyze the frequency dependence of temperature oscillation amplitude
  Requires only one Frequency-Domain Perturbation study step

## Slide 8: Results Average temperature oscillations
The results of time dependent study are in perfect agreement with the results of the frequency domain study.
Both approaches give the same results, but the frequency domain approach is much faster and has easier setup.
Average temperature oscillations computed with time dependent (blue curve) and frequency-domain perturbation (green dashed curve) solvers.

## Slide 9: Results Thermal Conductivity
The thermal conductivity is estimated by substituting two values from log-linear region of the curve into the Cahill’s equation
Selected frequencies f1=0.1 Hz and f2=10 Hz are defined in the Results > Parameters node
The frequency dependence of the average temperature oscillations: results of the time dependent study (the blue curve) and of the frequency domain study (green points)
Approach | Thermal conductivity
Exact value | 1.11 [W/m/K]
Time dependent | 1.1228 [W/m/K]
Frequency domain | 1.1228 [W/m/K]

## Slide 10: Conclusion
Both approaches give the same results for thermal conductivity, very close to the exact value used in the simulation.
The frequency domain approach is more effective because it gives accurate results but requires less time to compute.

## Slide 11: References
[1] Cahill, D.G. and Pohl R.O. (1987) Thermal conductivity of amorphous solids above the plateau. Phys. Rev. B 35(8), 4067-4073.
[2] F.P. Incropera, D.P. DeWitt, T.L. Bergman, and A.S. Lavine, Fundamentals of Heat and Mass Transfer, 6th ed., John Wiley & Sons, 2006.