## Slide 1: The Mixer App
Mixer Module

## Slide 2: Contents
Purpose
About the app
  User interface
  Tank types
  Impeller types
Some example results
The mixer app computes the flow field and eddy diffusivity in mixers and tank reactors

## Slide 3: Purpose
Simulate mixing efficiency in mixers and tank reactors
Select impellers, tank type, and baffles
Investigate operating conditions
Provide a starting point for own apps, for example to:
  Expand with more impellers and tank types
  Include non-Newtonian fluids
  Include two-phase flow
Results displayed in the apps user interface

## Slide 4: The User Interface
Set fluid properties
and operating conditions
Select tank and enter
tank dimensions
Set shaft dimensions
Send simulation report by e-mail when done
Simulation information
Reset all
Update geometry
Mesh
Run simulation
Read documentation
Create report
Show graphics

## Slide 5: The User Interface
Select existing impellers to change or remove
Enter impeller dimensions
Flip impeller
Enter number of blades,
cut, and fold blades
Update geometry
Add impellers
Show graphics

## Slide 6: Tank Types
All tanks can be equipped with an arbitrary number of rectangular baffles attached to the tank walls
Dished bottom
Flat bottom
Cone bottom

## Slide 7: Axial Impellers
Pitched
Pitched with folded blades
Pitched with constant pitch
Hydrofoil
Hydrofoil with constant pitch
C-shaped (Intermig®)
Intermig is a registered trademark of Ekato Holding GmbH

## Slide 8: Radial Impellers
Rushton turbine
Rushton with backswept blades
Smith turbine
Backswept
Anchor

## Slide 9: Great variety of Designs Possible for Pitched and Hydrofoil Impellers
Cut
Fillet and fold
Straight hydrofoil
Cut inner
Cut outer
Propeller type impeller using cuts and fillets
Fillets

## Slide 10: Embedded Model
Flow in rotating machinery using a y+ algebraic turbulence model
Frozen rotor approximation using arbitrary Lagrangian-Eulerian (ALE) formulation
Wall distance function and shear stress determines the eddy diffusivity
Free surface computation for small surface deformations

## Slide 11: Example Results
Eddy diffusivity, streamlines, and mixing time scales
Shape of free surface