## Slide 1: Notch Approximation to Low-Cycle Fatigue Analysis of a Cylinder with a Hole

## Slide 2: Model Background
A structural component is subjected to multi-axial cyclic loading. The stresses are above yield limit and localized plasticity occurs.
The elastoplastic response is computed using a method of notch approximation.
Fatigue is based on the stress-based Smith-Watson-Topper model.
This model demonstrates how to perform low-cycle fatigue in absence of plastic material data.

## Slide 3: Notch Approximation
Notch approximation is an effective way to perform fatigue evaluation since the elastoplastic response is based on an linear elastic analysis.
The elastic response is transformed using the Neuber correction into an elastoplastic state.
The full elastoplastic simulation it therefore not needed and the computation time is significantly reduced.

## Slide 4: Fatigue Prediction
The strain-based models are suitable for low-cycle fatigue.
The fatigue is evaluated with the Smith-Watson-Topper model.
The results based on the notch approximation can differ from the fatigue prediction of a full elastoplastic simulation. However they qualitatively capture the general fatigue trend.